## Slide 1: RISC-V Tutorial
Zhiming Zhang

## Slide 2: Outline
Verilator simulation
  Hello world!
  Spectre V1 example
  Configure your own BOOM -- SSE-RV example
  Cycle-by-cycle debugging
FPGA emulation
  Original BOOM SoC
  SSE-RV BOOM SoC
  General Vivado design chain
  Vivado integrated logic analyzer (ILA)
New microarchitectural attack replications on SonicBOOM
  Backend: FDiv covert channel
  Frontend: Spectre V4
Improvement of SSE-RV
  Overtainting issue
  Overuntainting issue
Extended SSE-RV

## Slide 3: Verilator Simulation
Hello world!
  Follow https://chipyard.readthedocs.io/en/latest/Chipyard-Basics/Initial-Repo-Setup.html#initial-repository-setup to setup the Chipyard environment to run Verilator
  Compile a SmallBoomConfig on Verilator
    Go to chipyard/sims/verilator, then
  Create a hello.c
  Compile hello.c using the riscv64-unknown-elf-gcc in chipyard/riscv-tools-install/bin
  Run Verilator
1)
2)

## Slide 4: Verilator Simulation
Spectre V1 attack example
  Understand the Spectre V1 code in https://github.com/sabbaghm/boom-attacks
  Compile Spectre V1
  Perform Spectre V1 attack on SonicBOOM
Secret retrieving!

## Slide 5: Verilator Simulation
Configure your own BOOM -- SSE-RV example
Find the SSE-RV protected BOOM core in Sequoia server /home/majid/unified_MajidSabbagh_PhD under SSE-RV/SonicBoom
Go to chipyard/generators/boom/src/main/scala
  Modify the Chisel source codes based on SSE-RV BOOM core
Original:
SSE-RV:
Involved files

## Slide 6: Verilator Simulation
Configure your own BOOM -- SSE-RV example
Source env.sh and compile a SmallBoomConfig
Test SSE-RV, you should see
  Hello world runs correctly
  Spectre V1 is mitigated
Leaking is prevented!

## Slide 7: Verilator Simulation
Debug example -- cycle-by-cycle log
In core.scala, add the following printfs to the Handle Cycle-by-Cycle Printouts section
Compile a SmallBoomConfig with debug enabled
Simulate hello world using the newly configured simulator-chipyard-SmallBoomConfig-debug
hello.log:

## Slide 8: Original BOOM SoC
Find the Xilinx Genesys-2 FPGA board in ISEC room463c
  Power up the board and connect both USB and UART ports with a computer
Go to https://github.com/eugene-tarassov/vivado-risc-v and follow the steps to program Genesys-2 with original BOOM-based SoC
  You can skip “Prepare the SD card” since there is already a card prepared
  Xilinx Vivado is installed in 463c server

## Slide 9: Original BOOM SoC
Login to the Debian system running on the FPGA board
  Through UART: sudo miniterm /dev/ttyUSB* 115200
  Through SSH: ssh debian@ipFPGA or ssh root@ipFPGA
  Username/password: debian/debian or root/root
  Uart transmission may bring in weird symbols but that is only a display issue
Hello world!
  Create a hello world c code on Debian
  Compile it using gcc and run the compiled executable
Run Spectre attacks on FPGA
  The FPGA-version of Spectre attacks are slightly different from the Verilator-version and can be found at: https://github.com/sabbaghm/sonicboom-attacks

## Slide 10: SSE-RV BOOM SoC
In the newly cloned vivado-risc-v repo, locate the BOOM generator at vivado-risc-v/generators/riscv-boom
Modify the Chisel source codes towards SSE-RV (Same as what we did in Verilator simulation)
Regenerate bitstream
  source /opt/Xilinx/Vivado/2020.1/settings64.sh
  make CONFIG=rocket64w1 BOARD=genesys2 bitstream
Program FPGA and boot the system (no need to reprepare SD card)
Perform Spectre attacks again to see if leakage is mitigated

## Slide 11: Vivado General Design Chain
Main design flow
Source hierarchy
Source file editing
Check errors, warnings, infos, …

## Slide 12: Vivado General Design Chain
To generate bitstream
  Run Synthesis  Run Implementation  Generate Bitstream
To program FPGA
  Go to Open Hardware Manger  Open Target
  Click on Program Device
Make sure the bitstream is correct, then click Program

## Slide 13: Integrated Logic Analyzer (ILA)
We can use Vivado ILA to help debugging FPGA design
Click on the left-hand side of Vivado GUI
  An IP Catalog subwindow is then added to the source editing area
Go to  
  A Customize IP window will show up

## Slide 14: Integrated Logic Analyzer (ILA)
In the Customize IP window
  Set up the Number of Probes
  Check Advanced Trigger
  Set up the width of each probe
  Click OK
In the following Generate Output Products window
  Choose Synthesis Options as Global
  Click Generate, the ILA module is then added to Design Sources

## Slide 15: Integrated Logic Analyzer (ILA)
Check the Verilog file of ILA module and instantiate it by conducting the ports
Rerun the design flow to generate a new bitstream
When programming the FPGA, a new Debug probes file is also included

## Slide 16: Integrated Logic Analyzer (ILA)
Now HARDWARE MANAGER window looks like this
Create a .tsm file to set up trigger conditions

## Slide 17: Integrated Logic Analyzer (ILA)
Check the option , then click , the waveform will be updated every time a triggering condition is met
For more details about ILA and programming .tsm trigger file, please check this video: https://youtu.be/_ljXMoGJ5iM

## Slide 18: New microarchitectural attack replications on SonicBOOM
FDiv covert channel
  Read the SpectreRewind paper at: https://arxiv.org/abs/2003.12208
  To better understand the how FDiv covert channel works on x86, go to its github: https://github.com/CSL-KU/SpectreRewind-PoC
Port FDiv channel to SonicBOOM
  Find the threshold determination code detect_spr.c at: TBD
  Compile detect_spr.c in FPGA and run (refer to Section 2 of this tutorial)
  You should see a hist.dat generated and the terminal output similar as:
    If you see error rate is too high, rerun the executable

## Slide 19: Port FDiv channel to SonicBOOM
Further verify the threshold
  Plot hist.dat (can use the matlab code at: TBD)
  Should see a clear threshold based on the plot
Transmit a secret byte using the FDiv channel
  Find the FDiv channel source code FDiv_test.c at: TBD
  Compile FDiv_test.c in FPGA and run
  Should see secret byte is successfully recovered

## Slide 20: Port FDiv channel to SonicBOOM
Spectre V1 + FDiv on SonicBOOM
  Combine Spectre V1 frontend with FDiv covert channel, the source code SpecV1_FDiv_withCond_V1.c can be found at: TBD
  Compile and run, a secret byte should be recovered as:

## Slide 21: New microarchitectural attack replications on SonicBOOM
Spectre V4 attack
  Understand Spectre V4 basics at: https://www.cyberus-technology.de/posts/2018-05-22-intel-store-load-spectre-vulnerability.html
  Github
  My Spectre V4 code SpectreV4_06292022.c (not complete) is in: TBD

## Slide 22: Improvement of SSE-RV
Read Majid’s SSE-RV paper to understand the original taint initialization scheme.
An “overtainting” issue is in Majid’s SSE-RV source code at /home/majid/unified_MajidSabbagh_PhD under SSE-RV/SonicBoom
  In his code, all speculative instructions’ destination registers are tainted.
  It is too aggressive because only speculative load instructions can steal secret from memory
One improvement is restricting the taint initialization only to speculative load instructions
  Find the BOOM core with this improvement at: TBD

## Slide 23: Improvement of SSE-RV
Read Majid’s SSE-RV paper to understand the original untainting scheme.
An “overuntainting” issue is SSE-RV untaints all registers when any speculative access instruction passes speculative status
Instructions remain speculative may be accidently marked as safe

## Slide 24: Improvement of SSE-RV
One improvement is we can now specifically untaint the destination registers of individual instructions
  We build connections between reorder buffer (ROB) and register file
  We check the speculative status for each in-flight instruction at runtime
  Track the destination registers of instructions that passed speculative status and untaint them
Find the BOOM core with this improvement at: TBD

## Slide 25: Extended SSE-RV
Extend the back end protection of SSE-RV
  Current SSE-RV only blocks cache covert channel
  Extended back end protection should be able to thwart port-contention channels
  Current strategy: the contention is originated from a secret-dependent branch, such branch should be blocked from issuing
  Specific implementation: rely on the taint-tracking of SSE-RV, a branch instruction should not be issued util its operands are untainted
Secret-dependent branch

## Slide 26: Extended SSE-RV
The incomplete source code is in: TBD
Further extension: The strategy may also be applied to a “tainted load” to replace global memory fencing of SSE-RV to further improve performance
  Refer to SSE-RV paper to understand the memory fence enforcement