## Slide 1: RISC-V Tutorial
Zhiming Zhang

## Slide 2: Outline
Verilator simulation
  Hello world!
  Spectre V1 example
  Configure your own BOOM -- SSE-RV example
  Cycle-by-cycle debugging
FPGA emulation
  Original BOOM SoC
  SSE-RV BOOM SoC
  General Vivado design chain
  Vivado integrated logic analyzer (ILA)
Microarchitectural attack replications on SonicBOOM
Extension of SSE-RV
Fuzzer development for SonicBOOM

## Slide 3: Verilator Simulation
Hello world!
  Follow https://chipyard.readthedocs.io/en/latest/Chipyard-Basics/Initial-Repo-Setup.html#initial-repository-setup to setup the Chipyard environment to run Verilator
  Compile a SmallBoomConfig on Verilator
    Go to chipyard/sims/verilator, then
  Create a hello.c
  Compile hello.c using the riscv64-unknown-elf-gcc in chipyard/riscv-tools-install/bin
  Run Verilator
1)
2)

## Slide 4: Verilator Simulation
Spectre V1 attack example
  Understand the Spectre V1 code in https://github.com/sabbaghm/boom-attacks
  Compile Spectre V1
  Perform Spectre V1 attack on SonicBOOM
Secret retrieving!

## Slide 5: Verilator Simulation
Configure your own BOOM -- SSE-RV example
Find the SSE-RV protected BOOM core in Sequoia server /home/majid/unified_MajidSabbagh_PhD under SSE-RV/SonicBoom
Go to chipyard/generators/boom/src/main/scala
  Modify the Chisel source codes based on SSE-RV BOOM core
Original:
SSE-RV:
Involved files

## Slide 6: Verilator Simulation
Configure your own BOOM -- SSE-RV example
Source env.sh and compile a SmallBoomConfig
Test SSE-RV, you should see
  Hello world runs correctly
  Spectre V1 is mitigated
Leaking is prevented!

## Slide 7: Verilator Simulation
Debug example -- cycle-by-cycle log
In core.scala, add the following printfs to the Handle Cycle-by-Cycle Printouts section
Compile a SmallBoomConfig with debug enabled
Simulate hello world using the newly configured simulator-chipyard-SmallBoomConfig-debug
hello.log:

## Slide 8: Original BOOM SoC
Find the Xilinx Genesys-2 FPGA board in ISEC room463c
  Power up the board and connect both USB and UART ports with a computer
Go to https://github.com/eugene-tarassov/vivado-risc-v and follow the steps to program Genesys-2 with original BOOM-based SoC
  You can skip “Prepare the SD card” since there is already a card prepared
  Xilinx Vivado is installed in 463c server

## Slide 9: Original BOOM SoC
Login to the Debian system running on the FPGA board
  Through UART: sudo miniterm /dev/ttyUSB* 115200
  Through SSH: ssh debian@ipFPGA or ssh root@ipFPGA
  Username/password: debian/debian or root/root
  Uart transmission may bring in weird symbols but that is only a display issue
Hello world!
  Create a hello world c code on Debian
  Compile it using gcc and run the compiled executable
Run Spectre attacks on FPGA
  The FPGA-version of Spectre attacks are slightly different from the Verilator-version and can be found at: https://github.com/sabbaghm/sonicboom-attacks

## Slide 10: SSE-RV BOOM SoC
In the newly cloned vivado-risc-v repo, locate the BOOM generator at vivado-risc-v/generators/riscv-boom
Modify the Chisel source codes towards SSE-RV (Same as what we did in Verilator simulation)
Regenerate bitstream
  source /opt/Xilinx/Vivado/2020.1/settings64.sh
  make CONFIG=rocket64w1 BOARD=genesys2 bitstream
Program FPGA and boot the system (no need to reprepare SD card)
Perform Spectre attacks again to see if leakage is mitigated

## Slide 11: Vivado General Design Chain
Main design flow
Source hierarchy
Source file editing
Check errors, warnings, infos, …

## Slide 12: Vivado General Design Chain
To generate bitstream
  Run Synthesis  Run Implementation  Generate Bitstream
To program FPGA
  Go to Open Hardware Manger  Open Target
  Click on Program Device
Make sure the bitstream is correct, then click Program

## Slide 13: Integrated Logic Analyzer (ILA)
We can use Vivado ILA to help debugging FPGA design
Click on the left-hand side of Vivado GUI
  An IP Catalog subwindow is then added to the source editing area
Go to  
  A Customize IP window will show up

## Slide 14: Integrated Logic Analyzer (ILA)
In the Customize IP window
  Set up the Number of Probes
  Check Advanced Trigger
  Set up the width of each probe
  Click OK
In the following Generate Output Products window
  Choose Synthesis Options as Global
  Click Generate, the ILA module is then added to Design Sources

## Slide 15: Integrated Logic Analyzer (ILA)
Check the Verilog file of ILA module and instantiate it by conducting the ports
Rerun the design flow to generate a new bitstream
When programming the FPGA, a new Debug probes file is also included

## Slide 16: Integrated Logic Analyzer (ILA)
Now HARDWARE MANAGER window looks like this
Create a .tsm file to set up trigger conditions

## Slide 17: Integrated Logic Analyzer (ILA)
Check the option , then click , the waveform will be updated every time a triggering condition is met
For more details about ILA and programming .tsm trigger file, please check this video: https://youtu.be/_ljXMoGJ5iM